## Slide 1
Advanced Time-domain Calibrations and Data-reduction Techniques with HST/COS
Justin Ely1, K. A. Bostroem1, John H. Debes1, 3, Svea Hernandez1, Philip Hodge1, Robert I. Jedrzejewski1, Kevin Lindsay1, Derck Massa1, 4, Cristina M. Oliveira1, 3, Steven V. Penton1, Charles R. Proffitt2, 1, Julia Roman-Duval1, 3, David J. Sahnow1, Hugues Sana1, 3, Paule Sonnentrucker1, 3, Joanna M. Taylor1
1. STSCI, 2. CSC, 3. ESA, 4. SSI
Abstract
The Hubble Space Telescope/Cosmic Origins Spectrograph (HST/COS) detectors have a time-tag mode of observation in which the arrival time of each photon is recorded individually. Although the COS calibration pipeline (CalCOS) makes use of this capability in many aspects of routine processing, there remains a number other ways that this information can be used to improve the calibration for specific science cases. This has led to the development of tools and techniques to perform additional calibrations that are not part of the standard data products output by CalCOS, but have been made available to the user. Here we demonstrate a few of these techniques including day/night filtering, extracting spectra on sub-exposure timescales, producing photometric light-curves, and performing additional dark-count screening.
TimeFilter
Tutorials
Running the calibration and analysis shown here can be a complicated process, and not very amenable to display in the poster format. As such, In-depth tutorials for each of the topics explained here can be found at the following location. https://github.com/justincely/AAS224
This link connects to a GitHub repository containing step-by-step demonstrations using the mentioned tools and techniques. Each tutorial is written in Python and contained in an iPython notebook such that they can be re-run and modified at will. PDF and HTML versions of the tutorials, this poster, all plots, and the raw datasets are also included.
Lightcurves
The standard CalCOS pipeline extracts 1D dispersed spectra as the final data products. The time information collected during data gathering, and used in subsequent processing, can instead be used to extract time-series lightcurves.
The
Code Repository
The library used to extract the lightcurves on this poster is available on both GitHub and the Python Package Index. You can find more information, download the source, or contribute to the library at the following:
http://justincely.github.io/lightcurve/
Splittag
The text will go here.
Pulse Height Filtering
The text will go here.
CORRTAG files
There are many data products associated with the CalCOS calibration pipeline, but one file at the heart of COS data is the *_corrtag_* file. This file contains a list of every event detected during an observation, along with a large amount of associated formation used in later processing: incident time, detector position, data quality, wavelength, and pulse-height amplitutde (PHA) to name just a few. Other extensions in the file also include tables of times with good data quality and a second-by-second accounting of various orbital parameters.
It is this file that makes possible the special calibrations mentioned here. Each one is a specialized re-arranging, slicing, or filtering of that event list and associated metadata followed by re-extraction with CalCOS or other specialized software. For more information, please review the COS Data Products section of the current Data Handbook.